## Slide 1: MIND: In-Network Memory Management for Disaggregated Data Centers
Seung-seob Lee, Yanpeng Yu, Yupeng Tang,
Anurag Khandelwal, Lin Zhong, Abhishek Bhattacharjee
Yale University
SOSP 21
2021.11.26 presented by GZ

## Slide 2: Resource Disggregation
CPU
MEM
GPU
CPU
MEM
GPU
CPU
MEM
GPU
[servers]

## Slide 3: Resource Disggregation
CPU
MEM
GPU
CPU
MEM
GPU
CPU
MEM
GPU
[servers]
Network
CPU
CPU
CPU
MEM
MEM
MEM
GPU
GPU
GPU
disaggregated blades
Benefits of resource disaggregation
* High resource utilization
* Easy to manage
* Elastic scalability

## Slide 4: Memory Disaggregation
• Need for memory disaggregation
• Timely problem
Low utilization
(as low as 30%)
Unbalanced Usage
(>70% of the time in clusters)
Energy Consumption
(up to 46% of avg. system)

## Slide 5: Memory Disaggregated Goals
Performace(CPU <-> Memory)
  high throughput & low latency
Transparent elasticity
  flexible resource allocation

## Slide 6: Existing Approaches
Performance
Transparent elasticity
Distributed shared memory (DSM)
Recent disaggregated memory schemes
DSM
Recent Disagg.
Ideal

## Slide 7: Key Insight : In-network memory management
Central location: global view & processing directly in the data path

## Slide 8: Key Insight : In-network memory management
Central location: global view & processing directly in the data path
Programming switching ASIC: flexible processing at line rate

## Slide 9: Key Insight : In-network memory management
Central location: global view & processing directly in the data path
Programming switching ASIC: flexible processing at line rate
Similarity between network functions and memory management

## Slide 10: MIND: In-network Memory management
CPU
CPU
CPU
Programable switch
Control plane
Data plane
Memory
Memory
Read, 0X1000

## Slide 11: MIND: In-network Memory management
CPU
CPU
CPU
Programable switch
Control plane
Data plane
Memory
Memory
Read, 0X1000
Address translation:
where is the data?

## Slide 12: MIND: In-network Memory management
CPU
CPU
CPU
Programable switch
Control plane
Data plane
Memory
Memory
Read, 0X1000
Address translation:
where is the data?
Memory protection
Is this access permitted or valid?

## Slide 13: MIND: In-network Memory management
CPU
CPU
CPU
Programable switch
Control plane
Data plane
Memory
Memory
Read, 0X1000
Address translation:
where is the data?
Memory protection
Is this access permitted or valid?
Cache coherency protocol:
How to keep data synchronized?

## Slide 14: Challenges in Building In-network MMU
Limited resources
  Limited size of in-network memory
    Tens of MB → not sufficient to store metadata in a traditional way
  Limited computation capability
    Switching ASIC → not sufficient to directly port traditional MMU functions

## Slide 15: Three Principle of system Design
P1-Decouple memory managemnet functionalities
P2-Leverage global view of network
P3-Exploit network-centric hardware primitives

## Slide 16: MIND overview: challenges and solutions

## Slide 17: MIND overview: challenges and solutions
CPU
CPU
Local DRAM as cache
NIC
MEM
MEM
NIC
MEM
MEM
NIC
CPU
CPU
Local DRAM as cache
NIC
CPU
CPU
Local DRAM as cache
NIC
CPU
CPU
Local DRAM as cache
NIC
Control plane
Memory allocation
Permission assignment
Directory entry allocation
Data plane
Cache directory
Memory protection
Address translation
Programmable switch
4KB page: too many entries
Huge page: load balancing&memory fragmentation
decoupling address translation and protection
translation blade-based & protection vma-based
use range partitions not page-based
use single virtual address space for all processes

## Slide 18: MIND overview: challenges and solutions
CPU
CPU
Local DRAM as cache
NIC
MEM
MEM
NIC
MEM
MEM
NIC
CPU
CPU
Local DRAM as cache
NIC
CPU
CPU
Local DRAM as cache
NIC
CPU
CPU
Local DRAM as cache
NIC
Control plane
Memory allocation
Permission assignment
Directory entry allocation
Data plane
Cache directory
Memory protection
Address translation
Programmable switch
4KB page: too many entries
Huge page: inflexiable protection
VMA-granularity protection
leverage TCAM-based parallel range matches in programmable switch ASIC to support <PDID, vma> match

## Slide 19: MIND overview: challenges and solutions
CPU
CPU
Local DRAM as cache
NIC
MEM
MEM
NIC
MEM
MEM
NIC
CPU
CPU
Local DRAM as cache
NIC
CPU
CPU
Local DRAM as cache
NIC
CPU
CPU
Local DRAM as cache
NIC
Control plane
Memory allocation
Permission assignment
Directory entry allocation
Data plane
Cache directory
Memory protection
Address translation
Programmable switch
Small cache line: too many entries
Large cache line: false sharing
Access granularity
Coherence granularity
-> Dynamic resizing
use multicast in switch to send
invalidate messages

## Slide 20: MIND overview: challenges and solutions
CPU
CPU
Local DRAM as cache
NIC
MEM
MEM
NIC
MEM
MEM
NIC
CPU
CPU
Local DRAM as cache
NIC
CPU
CPU
Local DRAM as cache
NIC
CPU
CPU
Local DRAM as cache
NIC
Control plane
Memory allocation
Permission assignment
Directory entry allocation
Data plane
Cache directory
Memory protection
Address translation
Programmable switch
New memory allocation

## Slide 21: Performance evaluation
Performance
Transparent elasticity
DSM
Recent Disagg.
MIND

## Slide 22: Conclusion and summary
Trade-off between resource elasticity and performance in memory disaggregation
Designed MIND, an in-network MMU by leveraging programmable network
prototype of MIND can match the performance of prior proposals and provide transparent elasticity